PRODUCT 8.4Vdc 1500mA SPS MODEL SW15C-08401500-KC PART NO. SW13-08401500-EKC4 DESIGNED NO. TAE-3338 VER: A CUSTOMER PWK DATE 2016-08-18 本 电 器 符合 MEETSAFETYSTD.， MEET ROHS MEET CEC STD. AC PIN： 2 希望回签日/EXPECTED FEEDBACK BEFORE： 2016年08月25日 发 行 印 *未签回而下订单即视同认可！ 生产工厂/MANUFACTOTRY 设计验证/日期 DESIGN VERIFIED BY 设计师/日期 DESIGNED BY 工程确认/日期 Engineering Verification BY QE 验证/日期 QE VERIFIED BY TAE

UPDATE REV

Will you please sign one copy of the specifications as having your approval and return it to us for our records.

We would like to point out that your release is directly influencing our bulk production start-up date.

If we do not hear from you within 14 days from the date of the most recent revision, we will assume your acceptance.

| REV | UPDATE | Detail | DATE |
| --- | --- | --- | --- |
| A |  | FIRST | 2016-08-18 |

# Index

- Scope  …………………………………………………………………………………………     4

- Electrical Characteristics test   …………………………………………………………………   4

2.1     Input Characteristic   ………………………………………………………………....    4

2.1.1  Input Voltage and Frequency  ………………………………………………………..    4

2.1.2  Input current   ……………………………………………………………...............…    4

2.1.3  Ac inrush current  …………………………………………………………………….    4

2.1.4  Input leakage current …………………………………………………………………    4

2.1.5  Efficiency …………………………………………………………………………….    4

2.1.6  Stand-by power consumption  …………………………………………………….….    4

2.2     Output Characteristic……………………………………………………….…………   5

2.2.1 Output voltage and current  ……………………………………………………………   5

2.2.2 Startup and Turn-on Delay …………………………………………………………….   5

2.2.3 Overshoot     ……………………………………………….…………………………..   5

2.2.4 Short-Circuit Protection (SCP) ………………………………………………..………   5

2.2.5 Over Current Protection (OCP) ………………………………………………………    5

2.2.6 Over Voltage Protection (OVP) ……………………………………………………….   5

3. EMC-Specification ……………………………………………………………………………...   6

4.   Safety details:  ………………………………………………………………………………......  6

5.   Mechanical Specifications ………………………………………………………………..……   6

5.1     Physical ………………………………………………………………………………..   6

5.2     Input and Output Configuration ……………………………………………………….   6

附页：

6.   DC Cord…………………………………………………………………………………………..1

7.   Production of appearance drawing  ……………………………………………………...……….1

8.   Label  ……………………………………………………………………………………………...1

9.   PE BAG……………………………………………………………………………………………1

- Packing……………………………………………………………………………………….…...2

# 1     Scope:

This document describes power supply unit for the I.T.E.. This document  covers all electrical, mechanical, environmental and testing aspects of the power supply unit. The power supply unit must comply with all of the requirements of this specification and the drawings

and specifications referenced here in.

# 2     Electrical Characteristic test:

## 2.1       Input Characteristics:

## 2.1.1   Input Voltage and Frequency

The power supply shall meet all specifications when powered from the following sources.

| Voltage Range | Line Frequency | Minimum Voltage | Maximum Voltage |
| --- | --- | --- | --- |
| 100-240Vac | 47 ~ 63 Hz | 90Vac | 264 Vac |

## 2.1.2    Input Current

The maximum input current shall be less than 1.0A.

## AC Inrush Current

At Full Load,25℃,Cold Start

| 115VAC,60Hz INPUT | NO damage shall be occurred and the input fuse shall not be blown up |
| --- | --- |
| 230VAC,50Hz INPUT |  |

## Input Leakage Current

The leakage current shall not exceed 0.25 mA.

## Efficiency

70% Minimum. at input 100-240Vac,100%Load. C.V.:7.5V.

## Stand-by power consumption

0.5W Max  At AC nominal input＠output min load

## 2.2   Output Characteristics:

## 2.2.1    Output Voltage and Current

The power supply shall have one regulated DC output of +8.4V.

The table below defines the total regulation band for the output, which includes line regulation, load regulation, transient response, and effects due to environmental conditions and aging. Voltage shall be measured at the power supply output connector

| Mode | Output Current Range | No-load Output Voltage range | Ripple Noise |
| --- | --- | --- | --- |
|  | Min. | Max. | Min. | Max. | Max. |
| C.V. | 1300mA | 1700mA | 8.35V | 8.47V | / |
| C.V.:7.5V, Iout=1500±200mA |  |  |  |
| 转灯电流Iout=250~500mA |  |  |  |

Ripple & Noise Test: Add 0.1uF/50V ceramic capacitor and 10uF/50V capacitor

across the output terminal.Measured with 20MHz Bandwidth

Oscilloscope.

## Startup and Turn-on Delay

Power supply shall be able to start up into a resistive load up to the maximum rated current with maximum load capacitance of 1,000uF. The elapsed time between the application of input power and the attainment of output voltage to the nominal value shall not exceed 3 second.

## Overshoot

At turn on, the output voltage shall not exceed steady state by more than 10%.

## Short-Circuit Protection

The Adapter is protected that a short happened between the output terminals and shall not result

in a fire hazard ,and will be normal operation automatically while the short is removed

## Over Current Protection

No safety hazard

## Over Voltage Protection

No safety hazard

# 3     EMC-Specification

## Noise-suppressed acc:               EN 55022

# Safety details:

Standards/class                               :                  EN60950      ClassII

Voltage rating                     input    :                 100Vac-240Vac  50/60Hz

Output  :                8.4Vdc 1500mA

High-voltage test                           :                  ≥3.3KV/3S

Leakage current                             :                 Maximum leakage current is10mA

Application range                          :                 Information technology equipment

Including electrical business equipment

Ambient temperature                     :                 0°C  to  +40° C  ,  10 to 90%  rhd

# 5     Mechanical Specifications

## 5.1   Physical

Case material:	PC or PC+ABS

Dimensions:	  70mm(L) x 41.5mm(W) x 30mm(H) (not include input pins)

## 5.2   Input and Output Configuration

Input Pin:	EK pins

Output Connector:	2.1*5.5*10mm “H”type 音叉带出台

Polarity:	Center positive

Lead:	1.5m  AWM2464 22AWG

# DC Cord drawing（black）:

# Production of appearance drawing(black):

## Label:

备注：

      - 铭牌颜色：灰底黑字.

# Text boxes

TOP-ASIA ELECTRONICS GROUP

SPECIFICATION  FOR  APPROVAL